## Slide 1: Proposed Heavy Vehicle Testbed Updates
A Presentation by Blake Fusick

## Slide 2: Contributions
Efficiency
  Data Transfer Improvements (only logging on front interface)
    Less Overhead (Quicker Data Transfer)
    Leads to Simplicity
  Parsing Data on Front Interface for Plots
    Rather than Parsing and Sending from BeagleBone
Testing
  Check if Frames are Dropped
  Determine Latency
  Log Format
    https://github.com/Heavy-Vehicle-Networking-At-U-Tulsa/NMFTA-CAN-Logger
  Perform Diagnostics Tests
Solve Timestamp Problem
  Power Loss Resets BeagleBones Causing Scheduling Issues
  Connect BeagleBones to Server with Timestamp

## Slide 3: More Contributions
Additional Features
  Viewing/Filtering CAN Messages on Front Interface
  Loop all Simulation Commands (Loop Drive)
  Create Default Drives
Simplicity
  Rather than Start 5 Different Scripts, Start Testbed with One
  Eliminate unused Files/Code Leftover
Live Data/Commands (Ambitious Goal)

## Slide 4: Testbed

## Slide 5: ECUs and Simulators

## Slide 6: Network Control Nodes

## Slide 7: Data Transfer Improvements

## Slide 8: Can Bus Traffic Logger

## Slide 9: Current CAN Bus Traffic Logger
Request Handling
  Wait for Requests from Experiment Handler
    Start Logging Data Locally
  Wait for Requests from Front Interface
    Send Experiment Data
    Send Plottable Data
    Delete Experiments
Types of Requests
  DeleteExperiment
  GetExperiment
  GetAxleBasedVehicleSpeed
  StartLogging

## Slide 10: Proposed CAN Bus Traffic Logger
Request Handling
  Wait for Requests from Front Interface
    StartCanStream
Types of Requests
  StartCanStream HTTP POST
    JSON
      “function”: “on” or “off”

## Slide 11: Experiment Handler

## Slide 12: Current Experiment Handler
Tasks
  Send CAN Frames
  Send SSS2 Commands
  Send HTTP Request to Logger
  Use Commands at Specified Delays
  Wait for HTTP POST Experiment Request
    Starts the Experiment

## Slide 13: Proposed Experiment Handler
Tasks
  Send CAN Frames at Specified Delays
  Send SSS2 Commands at Specified Delays
  Wait for HTTP POST Experiment Request
Functionality
  No Experiment Objects on Handler
  Just JSON with Commands at Specified Delays
  Time = 0 => Perform Command Immediately

## Slide 14: User Interface

## Slide 15: Old User Interface
  Browser-Based Interface
    User-Friendly
    Take Input from Users
    Login/Users
      Associated with Experiments
  Scheduling Tasks
  Communication
    Start Experiment
    Retrieve Logs
    Retrieve Plot Data
  Database
    Store Experiments/Data/Plot Data
  Remote Access

## Slide 16: New User Interface
  Browser-Based Interface
    User-Friendly
    Take Input from Users
    Login/Users
      Associated with Experiments
  Scheduling Tasks
  Communication
    Start Experiment
    Retrieve Logs
    Retrieve Plot Data
  Database
    Store Experiments/Data/Plot Data
  Remote Access

## Slide 17: User Interface
Selecting a Plot and Parsing on User Interface

## Slide 18: My Experiments Page

## Slide 19: Run Results of an Experiment

## Slide 20: View Plots Page Proposal
Interface
Parameter
Units

## Slide 21: Testing and Timestamp Issues
Testing
  Check if Frames are Dropped (full bus load)
    4 Bytes of Tx Counter
  Determine Latency
    4 Bytes of Timestamp
  Log Format
    https://github.com/Heavy-Vehicle-Networking-At-U-Tulsa/NMFTA-CAN-Logger
  Perform Diagnostics Tests
Solve Timestamp Problem
  Power Loss Resets BeagleBones Causing Scheduling Issues
  Connect BeagleBones to Server with Timestamp

## Slide 22: Additional Features
Additional Features
  Viewing/Filtering CAN Messages on Front Interface
  Loop all Simulation Commands (Loop Drive)
  Create Default Drives

## Slide 23: Run Results of an Experiment
View Log

## Slide 24: View Logs Page
Interface
Priority
PGN
DA
SA
Full ID
can1 6 FEF1 FF (Broadcast) 00 (Engine) 18FEF100 11 22 33 44 55 66 77 88
can0 3 F004 FF (Broadcast) 00 (Engine) 18F00400 00 11 22 33 44 55 66 77

## Slide 25: User Interface
Live Data

## Slide 26: My Experiments Page
View Live Data

## Slide 27: View Live Data Page
Interface
Priority
PGN
DA
SA
Full ID
can1 6 FEF1 FF (Broadcast) 00 (Engine) 18FEF100 11 22 33 44 55 66 77 88
can0 3 F004 FF (Broadcast) 00 (Engine) 18F00400 00 11 22 33 44 55 66 77
Data
Plots

## Slide 28: View Live Plots Page
Interface
Parameter
Data
Plots
Units

## Slide 29: View Live Data Command Inputs (Scrolled Down)
Interface
ID:
Data:
Send CAN Message
Interface
ID:
Data:
Gap:
Extended Bit
RTR Bit
Loop CAN Message
Type
Parameters:
Send Simulation Command
VIN:
Update VIN
Governor Speed:
Update Gov Speed
Send Single CAN Message
Send Looped CAN Messages
Send Simulation Command
Parameter Updates
View Active Looped Messages

## Slide 30: View Active Cangens Page
can1 –eI 18FEF100 –D 1122334455667788 –g 350
can1 –eI 18F00400 –g 100
STOP
STOP
STOP
STOP

## Slide 31: Stop Cangen Page
Are you sure you want to stop this cangen?
can1 –eI 18F00400 –g 100
STOP
NO
STOP
YES

## Slide 32: Summary of Contributions
  Efficiency
  Testing
  Extra Features
  Simplicity
  Live Data

## Slide 33: Questions?
https://www.duskyillusions.com/niche-niche-question/man-with-question-04/